## Slide 1: Spectre
Alex Young

## Slide 2: Part 1: Introduction

## Slide 3: What is Spectre?
source: https://meltdownattack.com/

## Slide 4: Who is impacted by Spectre?
All modern CPUs
Cloud-based servers

## Slide 5: Why is Spectre important?
The widespread impact
Everything is ‘working as intended’
“As it is not easy to fix, it will haunt us for quite some time.”

## Slide 6: When/Where was Spectre discovered?
Google Project Zero
University Researchers
Meltdown and Spectre

## Slide 7: Part 2: Understanding how Spectre Works

## Slide 8: The Evolution of the CPU
source: https://www.researchgate.net/figure/Evolution-of-multi-core-processors-1_fig1_281534326

## Slide 9: Out-of-order Execution
Reduce wasted clock cycles
Instructions that read from memory take more time

## Slide 10: Speculative Execution
source: https://spectrum.ieee.org/how-the-spectre-and-meltdown-hacks-really-worked

## Slide 11: The Cache
The CPU cache is a hardware cache used to quickly access memory
The cache can be targeted by shared resource attacks, specifically timing attacks

## Slide 12: Putting it all together
Redirect speculative execution
Cache timing attack

## Slide 13: Part 3: Spectre Attacks

## Slide 14: Branch Redirection
if (x < array1_size) y = array2[array1[x] * 4096]
x is initial ran using in-bounds values
x is ran using an out-of-bound location of the secret memory that we want to access
source: https://spectreattack.com/spectre.pdf

## Slide 15: Flush and Reload
Flush+Reload, Evict+Reload
clflush
timing

## Slide 16: Results
Can run 188 instructions (192 in buffer) ahead of instruction pointer
10 KB/s can be read

## Slide 17: Variations
Poisoning Indirect Branches
9 more variants in 2019
Micro-Op cache
source: https://spectreattack.com/spectre.pdf

## Slide 18: Part 4: Spectre Defense/Mitigation

## Slide 19: Preventing Speculative Execution on Protected Data
Preventing speculative execution in general
Executing separate web pages in different processes
Using a bit mask on array indices to limit accessing out-of-bounds memory addresses

## Slide 20: Further Defense
Preventing branches from being poisoned
Prevented side-channels attacks through the cache

## Slide 21: Mitigation in Use
MIT DAWG
Linux KPTI

## Slide 22: Part 5: Conclusion

## Slide 23: Key Takeaways
Keep your software up to date
CPU design

## Slide 24: Sources
https://spectreattack.com/spectre.pdf
https://spectrum.ieee.org/how-the-spectre-and-meltdown-hacks-really-worked
https://www.sciencedaily.com/releases/2021/04/210430165903.htm
https://www.techrepublic.com/article/spectre-and-meltdown-explained-a-comprehensive-guide-for-professionals/

## Slide 25: Thank you for watching!